## Slide 1
PC Motherboard

## Slide 2: Moore’s Law
Pre early 2000: frequency x 2 every 18 months
Post 2005: core count x 2 every 18 months
Reference: Ahmet Ceyhan, Interconnects for Future Technology Generations: CMOS with Copper/Low-κ and Beyond, PhD Thesis, 2018

## Slide 3: Modern Multi-core Processor
One processor chip with multiple cores
Shared & core- private caches
Your desktop computer today:

## Slide 5: Hardware Threads
Hyper-threading (usually can be disabled)
  Presented to the OS as additional “cores” or “CPUs”
Processor
Core
Cache
Core
OS view: 4 “CPUs” but 2 physical cores

## Slide 6: Multi-socket: even more parallelism
In the cloud and enterprises: multi-socket
Multiple processors in each server
Socket to place a multicore processor
Usually 4-32 cores per processor
Memory slots
Memory slots
Memory slots
Memory slots
Socket
Socket
Socket
Socket
https://www.servethehome.com/supermicro-h8qgif-review-quad-g34-motherboard/supermicro-h8qgi-f-overview/
Mainstream database servers: 2 – 4 sockets
Very high-end/mission critical: 8-32 sockets

## Slide 7: Non-Uniform Memory Access (NUMA)
NUMA node:
A processor + local memory
Processor
Core
Core
Core
Core
Cache
Processor
Core
Core
Core
Core
Cache
Processor
Core
Core
Core
Core
Cache
Processor
Core
Core
Core
Core
Cache
Memory
Memory
Memory
Memory
Interconnect: communication medium that links
Processors to processors
Processors to memory
E.g., Intel QPI/UPI, AMD HyperTransport
Accessing local memory is faster than remote memory in other NUMA nodes, i.e., speed is not uniform
 “NUMA effect”

## Slide 8: Memory/Storage Hierarchy
    higher
    lower
Cost per bit &
Performance
    smaller
Capacity
    larger
Volatile
L1 Cache
Registers
L2 Cache
L3 Cache
Main memory
Persistent memory
Flash/disk
CPU
Non-volatile
Volatile
~4 cycles
~10 cycles
~60 cycles
20-50ns
50-300ns
us, ms…
1 cycle
Must bring data from storage to memory for CPU to access
Tape